Appendix C

Sample Format for System Verification and

Start-Up Checklists

NOTES TO APPENDIX C

This appendix contains sample systems verification and start-up checklists for a selection of equipment used frequently in typical HVAC systems.

There is no intention in the appendix to provide sample checklists for all possible equipment included in any design. These checklists are intended to illustrate a level of detail that is appropriate in good commissioning practice, and to suggest a practical format. As such, they contain typical items that are often required to be included in the inspections and checks carried out, and documented, prior to and during equipment start-up.

The sample checklists are generic; thus they do not apply to any specific project, and so the list of check items is generic, not specific. Commissioning authorities must develop systems verification and start-up checklists for every piece of equipment within the scope of any commissioning project, and those checklists must include all items included in the specific design that require checking.

There is a Table of Contents on the next page listing the sample checklists included in this appendix.

ACG assumes no responsibility for how the material in this Appendix may be utilized by users of the Guideline; the users assume full responsibility for any and all liability that may arise from any reference to, or use of, this material.

Table of Contents

Air Handling Unit	4

Controls Air Compressor	5

Hot Water Boiler	6

Chiller	7

Heating and Cooling Coils	8

Cooling Tower	9

Exhaust Fan	10

Fan Powered Variable Air Volume Boxes	11

Unitary Heat Pump - Water Source	12

Pumps	13

Return Fan	14

Roof Top Unit - Gas Heat/Dx Cooling	15

Supply Fan	16

Variable Air Volume Boxes	17

Point to Point Checks	18

# AIR HANDLING UNIT

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Seismic restraints |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Plenums clean and free of loose material |  |  |
| Temporary start-up filters |  |  |
| Fire & balance dampers positioned |  |  |
| Duct system tested and cleaned |  |  |
| Access doors, Insulation and interior lights |  |  |
| Local valving/piping (HWS, CHWS, steam, condensate, drains) |  |  |
| Drain pans |  |  |
| Heating and cooling coils |  |  |
| Failed position of heating coil valve-open to coil |  |  |
| Failed position of cooling coil valve-closed to coil |  |  |
| Outside air, return air and mixed air dampers |  |  |
| Humidifier |  |  |
| Building & fan room cleanliness |  |  |
| Filter bank, DP switch gauge and photohelics |  |  |
| Electrical wiring complete |  |  |
| Motor rated for VSD service |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Instrumentation (temperature, volume, pressure & humidity ) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| VSD Start-up by manufacturer's representative |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Freeze protection operational |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |
| Final operating filters installed |  |  |

# CONTROLS AIR COMPRESSOR

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Seismic restraints |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Local valving/piping (air, condensate, drains) |  |  |
| Bypass piping around dryer and filter |  |  |
| Intake air filter |  |  |
| Inlet and outlet air silencers |  |  |
| High pressure relief valve |  |  |
| Status indicators- local/remote. |  |  |
| Pressure gauges. |  |  |
| Air receiver with automatic and manual drains |  |  |
| Duplex oil and particle separators. |  |  |
| Duplex Micron discharge filters |  |  |
| Flexible air connection |  |  |
| Refrigerated air dryer. |  |  |
| Pressure reducing valve |  |  |
| Isolation valve on each high pressure line. |  |  |
| Electrical wiring complete |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Local starters |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start-up by manufacturer's rep. (report attached) |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |

# Hot Water Boiler

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Boiler certificate / registration (copy attached) |  |  |
| Mounting/support system |  |  |
| Seismic restraints |  |  |
| Maintenance clearance |  |  |
| Local valving/piping correct (including expansion tanks and make-up water). |  |  |
| Chemical cleaning and treatment (report attached) |  |  |
| Temperature and pressure gauges |  |  |
| Pressure relief valve |  |  |
| Pressurization and leak tests |  |  |
| Blowdown system |  |  |
| Safety interlocks- low water and high temperature |  |  |
| Combustion air supply and ventilation |  |  |
| Insulation/lagging |  |  |
| Stack and breaching |  |  |
| Combustion chamber inspection |  |  |
| Fuel system (including emergency shutdown and gas inspection certificate) |  |  |
| Electrical wiring |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start HWS pumps to create load. |  |  |
| Start boiler circulation pumps. |  |  |
| Boiler startup by supplier |  |  |
| Supplier certificate or log provided for start-up and all specified and regulatory tests. |  |  |

# Chiller

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system |  |  |
| Seismic restraints |  |  |
| Maintenance clearance |  |  |
| Local valving/piping correct (including expansion tanks, make-up water and identification). |  |  |
| Pressurization and leak tests |  |  |
| Supplier pre-start (including charging the system) (report attached) |  |  |
| Chemical cleaning and treatment (report attached) |  |  |
| Insulation/lagging |  |  |
| Refrigerant relief valve |  |  |
| Temperature and pressure gauges |  |  |
| Flow switches - safety interlocks |  |  |
| Temperature sensors - safety interlocks |  |  |
| UL and ASME approvals |  |  |
| Control/diagnostic/programmable module |  |  |
| DDC interface with specified points e.g. chilled water setpoint and demand limiter analogue inputs, and % load, run status and alarm outputs |  |  |
| Electrical wiring |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start condenser water system |  |  |
| Start chilled water system to create load |  |  |
| Chiller startup by supplier |  |  |
| Modulation through specified range |  |  |
| Safety interlocks |  |  |
| Supplier certificate or log provided for start-up and all specified and regulatory tests |  |  |

# HEATING AND COOLING COILS

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Mounting/support system |  |  |
| Seismic restraints |  |  |
| Building & fan room cleanliness |  |  |
| Plenums clean and free of loose material |  |  |
| Duct system tested and cleaned |  |  |
| Fire & balance dampers positioned |  |  |
| Local valving/piping (HWS, CHWS, steam, condensate, drains) |  |  |
| Drain pans |  |  |
| Coils clean, fins straight and not damaged or corroded. |  |  |
| Water system cleaned & treated (report attached) |  |  |
| Strainers - construction screens removed. |  |  |
| Failed position of heating coil valve-open to coil |  |  |
| Failed position of cooling coil valve-closed to coil |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Freeze protection operational |  |  |
| Use Point-to-Point Checklist to record: |  |  |
| Water inlet temperature: __________(F |  |  |
| Water discharge temperature: __________(F |  |  |
| Air inlet temperature: __________(F |  |  |
| Air discharge temperature: __________(F |  |  |

# Cooling Tower

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system/vibration isolation |  |  |
| Seismic restraints |  |  |
| Maintenance clearance and access panels |  |  |
| Local valving/piping correct (including make-up water, meter, back flow preventer and identification). |  |  |
| Cooling tower leak test |  |  |
| Sump clean and free of loose material |  |  |
| Blowdown, drain and overflow system |  |  |
| Chemical cleaning & treatment (report attached) |  |  |
| Temperature gauges |  |  |
| Temperature sensors |  |  |
| Vibration sensor |  |  |
| Sump heater aquastat. |  |  |
| Sump heater, low water and high temp. cutout. |  |  |
| Lubrication |  |  |
| Vanes or dampers |  |  |
| High and low speed motors (or VSD) |  |  |
| Motor guards. |  |  |
| Sheaves and belts, alignment and tension |  |  |
| Freedom of rotation |  |  |
| Electrical wiring (complete) |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Local control panel with DDC interface |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start cooling tower fans |  |  |
| Direction of rotation |  |  |
| Motor Amps - Rated: Actual : |  |  |
| Motor Volts - Rated: Actual : |  |  |
| Start condenser water pumps |  |  |
| Modulate or stage cooling tower fans and/or vanes |  |  |
| Vibration & noise level acceptable |  |  |

# Exhaust fan

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Flexible connections |  |  |
| Seismic restraints |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Plenum/volute clean and free of loose material |  |  |
| Duct system tested and cleaned |  |  |
| Fire & balance dampers positioned |  |  |
| Exhaust louvers tested (gravity or motorized) |  |  |
| Building & fan room cleanliness |  |  |
| Electrical wiring |  |  |
| Motor rated for VSD service |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start-up by manufacturer's rep. (report attached) |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |

# Fan Powered Variable Air Volume Boxes

| PRE-START-UP INSPECTION |
| --- |
| Check the following equipment for: | VAV 1 | VAV 2 | VAV 3 | VAV 4 | VAV 5 |
| Local valving and piping |  |  |  |  |  |
| Local ductwork |  |  |  |  |  |
| Mounting support and seismic system |  |  |  |  |  |
| Maintenance access, access doors and insulation |  |  |  |  |  |
| Valve operation (reheat coil) |  |  |  |  |  |
| Damper operation |  |  |  |  |  |
| Sensor location and operation |  |  |  |  |  |
| Fan freedom of rotation |  |  |  |  |  |
| Electrical wiring complete |  |  |  |  |  |
| Overload protection (sized correctly) |  |  |  |  |  |
| Disconnect switch (tested) |  |  |  |  |  |
| Control system - point to point checks complete |  |  |  |  |  |
| Building cleanliness |  |  |  |  |  |
| START-UP |  |  |  |  |  |
| Start air handling system (see separate checklist) |  |  |  |  |  |
| Local fan direction of rotation |  |  |  |  |  |
| Electrical interlocks - stop/start |  |  |  |  |  |
| Speed selector switch |  |  |  |  |  |
| Local air leakage acceptable |  |  |  |  |  |
| Vibration & noise level acceptable |  |  |  |  |  |
| Motor Amps - Rated: Actual: |  |  |  |  |  |
| Motor Volts - Rated : Actual : |  |  |  |  |  |
| Final operating filters installed |  |  |  |  |  |

# Unitary Heat Pump - Water Source

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Seismic restraints |  |  |
| Lubrication |  |  |
| Temporary start-up filter |  |  |
| Access doors and insulation |  |  |
| Duct system completed and cleaned |  |  |
| Fire & balance dampers positioned |  |  |
| D/X coil, water/refrigerant heat exchanger, reversing valve, compressor |  |  |
| Water supply piping |  |  |
| Strainer, isolation and balance valve(s) |  |  |
| Drain piping |  |  |
| Drain pan |  |  |
| Fan freedom of rotation |  |  |
| Building cleanliness |  |  |
| Electrical wiring complete |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Local heating/cooling thermostat |  |  |
| START-UP |  |  |
| Start-up by manufacturer's representative and certificate or log provided |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Fan speed selector switch |  |  |
| No water or condensate leakage |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |
| Final operating filters installed |  |  |

# PUMPS

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Piping and valving |  |  |
| Seismic restraints |  |  |
| Mounting/support system and vibration isolation |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Electrical wiring |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| HWS or CHWS available |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |

# Return fan

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Flexible connections |  |  |
| Seismic restraints |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Plenums clean and free of loose material |  |  |
| Duct system tested and cleaned |  |  |
| Fire & balance dampers positioned |  |  |
| Building & fan room cleanliness |  |  |
| Electrical wiring |  |  |
| Motor rated for VSD service |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start-up by manufacturer's rep. (report attached) |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |

# Roof Top Unit - Gas Heat/DX Cooling

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Mounting/support system and vibration isolation |  |  |
| Seismic restraints |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Plenums clean and free of loose material |  |  |
| Temporary start-up filters |  |  |
| Fire & balance dampers positioned |  |  |
| Access doors, Insulation and interior lights |  |  |
| Filter bank, DP switch gauge and photohelics |  |  |
| Local valving/piping (gas, condensate, pans, drains) |  |  |
| Motorized dampers |  |  |
| D/X expansion (cooling) coil and compressor |  |  |
| D/X condensing coil and fans |  |  |
| Gas piping and valving complete |  |  |
| Gas inspection certificate |  |  |
| Regulatory authority approved installation and burner control (certificate available) |  |  |
| Building cleanliness |  |  |
| Electrical wiring complete |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Local control module with DDC interface |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| Start-up by manufacturer's representative with report and certificate or log provided |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |
| Final operating filters installed |  |  |

# Supply Fan

| ITEM | ( | COMMENTS |
| --- | --- | --- |
| PRE-START-UP INSPECTION |  |  |
| Commissioning lock-out procedures reviewed |  |  |
| Operation and maintenance information |  |  |
| Electrical wiring |  |  |
| Motor rated for VSD service |  |  |
| Overload protection (sized correctly) |  |  |
| Disconnect switch (tested) |  |  |
| Mounting/support system and vibration isolation |  |  |
| Seismic restraints |  |  |
| Flexible connections |  |  |
| Equipment guards |  |  |
| Alignment & V-belt tension |  |  |
| Freedom of rotation |  |  |
| Lubrication |  |  |
| Plenums clean and free of loose material |  |  |
| Temporary start-up filters |  |  |
| Fire & balance dampers positioned |  |  |
| Inlet louvers tested (gravity or motorized) |  |  |
| Duct system tested and cleaned |  |  |
| Access doors, Insulation and interior lights |  |  |
| Building & fan room cleanliness |  |  |
| Filter bank, DP switch gauge and photohelics |  |  |
| Instrumentation (temperature, volume, pressure & humidity ) |  |  |
| Control system - point to point checks complete |  |  |
| START-UP |  |  |
| VSD Start-up by manufacturer's rep. (report attached) |  |  |
| Direction of rotation |  |  |
| Electrical interlocks - stop/start |  |  |
| Freeze protection operational |  |  |
| Local air leakage acceptable |  |  |
| Vibration & noise level acceptable |  |  |
| Motor Amps - Rated : Actual : |  |  |
| Motor Volts - Rated : Actual : |  |  |
| Final operating filters installed |  |  |

# Variable Air Volume Boxes

| PRE-START-UP INSPECTION |
| --- |
| Check the following equipment for: |
| local valving and piping |
| local ductwork |
| mounting support and seismic system |
| maintenance access |
| valve operation |
| damper operation |
| sensor location and operation |
| Control system - point to point checks complete |
| Building cleanliness |
| Start-up |
| Start air handling system (see separate checklist) |
| Local air leakage acceptable |
| Unit ID | Room | Reheat | Ducting | Valving & Piping | Mounting Support Seismic | Maint. access | Valve operation | Damper operation | Airflow Sensor | Temp. Sensor |

# Point to Point Checks

| Point | Output | Input | Accept | Comment |
| --- | --- | --- | --- | --- |
| Description | Name | DO | AI 0% | AI 50% | AI 100% | DI | AI | Y/N |  |

# Text boxes

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment Name/Tag:		Location:

System/Area Served:		Related Equipment:

Pre-start checks by: 				Date:

Start-up checks by: 				Date:

print name	signature

PROJECT:

Equipment/System:		Location:

Checked by: 				Date:

Verified by: 				Date:

print name	signature